## Slide 1
ECE 4755
Final Project
10-point DFT and IDFT of the Lab 7 speech signal
and impulse response
Wayne Blaylock October 5, 2026

## Slide 2
What the project covers
ECE 4755 Final Project | Wayne Blaylock
2
Q1–Q4
10-point DFT and IDFT of speech.wav in MATLAB and in C, then plot the C results.
Q5
Same DFT, IDFT, and plots for impulse.wav.
Q6–Q8
DFT of both excerpts on the DSPLab, then the product and its IDFT on the scope.
Q9–Q10
Plot the board product in MATLAB, then repeat the product on the full files and compare.

## Slide 3
Method
ECE 4755 Final Project | Wayne Blaylock
3
Blocks of 10 samples. Last block is zero-padded. No fft or ifft.
X[k] = Σ x[n] exp(−j 2π k n / 10)
x[n] = (1/10) Σ X[k] exp(+j 2π k n / 10)
Y[k] = X[k] H[k], then IDFT for the circular convolution
speech.wav
182,932 samples, 44.1 kHz, 4.148 s, 8 pad samples
impulse.wav
130,036 samples, 44.1 kHz, 2.949 s, 4 pad samples
Board excerpts
Speech at sample 43968, impulse at sample 55680, 256 samples each
DSPLab
C5509A, dsplab55.gel, D/A 10 kHz, FIFO 256, signed

## Slide 4
Q1 MATLAB speech DFT and IDFT
ECE 4755 Final Project | Wayne Blaylock
4
IDFT error after dropping the pad is 2.78e-16. Bin spacing is 4,410 Hz, so one block only shows a coarse spectrum.

## Slide 5
Q2–Q4 Floating-point C on speech.wav
ECE 4755 Final Project | Wayne Blaylock
5
Left: C IDFT on the original. Right: concatenated C DFT magnitude. Segment 4500 matches a MATLAB DFT of the same block.

## Slide 6
Q5 Same procedure on impulse.wav
ECE 4755 Final Project | Wayne Blaylock
6
MATLAB IDFT and C IDFT both match impulse.wav. The impulse spectrum is broader than the speech spectrum.

## Slide 7
Q6 10-point DFT on the DSPLab scope
ECE 4755 Final Project | Wayne Blaylock
7
D0 released: speech excerpt. D0 pressed: impulse excerpt. Each bin is held for 25 samples. Scope scale is relative.
Speech energy is in the low bins. The impulse excerpt is more spread across the 10 bins.

## Slide 8
Q7–Q8 Product and IDFT on the DSPLab
ECE 4755 Final Project | Wayne Blaylock
8
Left: average |X[k] H[k]|. Right: IDFT of that product, a 10-point circular convolution. Spikes are the large blocks after DAC scaling.

## Slide 9
Q9 MATLAB plots of the Q7 and Q8 results
ECE 4755 Final Project | Wayne Blaylock
9
Same excerpts as the board. Shapes match the scope photos. Counts do not, because the DAC auto-scales.

## Slide 10
Q10 Full-file product, then compare
ECE 4755 Final Project | Wayne Blaylock
10
Left and center are the full files, time-aligned. Right is the board excerpts and matches Q9. The full-file result is the same method, not the same waveform, because the excerpts do not start at the same sample.
IDFT of each product is a circular convolution of that 10-sample pair, not one linear convolution of the whole files.

## Slide 11
Conclusions
ECE 4755 Final Project | Wayne Blaylock
11
1
10-point DFT and IDFT, from the sum, reconstruct speech.wav and impulse.wav.
2
C text files match the MATLAB transforms for both signals.
3
The board can only hold excerpts. D0 switches speech and impulse on the scope.
4
X[k] H[k] followed by the IDFT is a circular convolution per block.
5
The excerpt check matches the board plots. The full-file product does not, and should not.